VFOSSIL - An OS/2-Subset Video FOSSIL Appendage

                         Version 1.00,  May 23,  1988

                       Rick Moore,  Solar Wind Computing
                          FidoNet Address:  1:115/333





                 FidoNet Standards Committee index:  FSC-0021





















 Copyright (C) 1988, Rick Moore,  Homewood,  IL, 60430. All rights reserved.

 This document may be distributed freely as long as it is distributed in its
 original,  unmodified form.


VFOSSIL - An OS/2-Subset Video FOSSIL Appendage                         FSC-0021
                                                                         Page  2


VFOSSIL design criteria:

The VFOSSIL appendage proposed here is designed to be an compatible subset of
the OS/2 VIO subsystem.  All services are proper subsets of the equivalent OS/2
VIO API's,  and if you stick to the services defined in this document,  you
will be able to compile and run your programs with very minor changes in an
OS/2 environment.

VFOSSIL (and OS/2 VIO at this time) only supports text modes.  It is possible
to use the "set mode" service to set a graphics mode,  but that is the only
support for pixel-oriented graphics functions provided by VFOSSIL.  The minimum
environment supported by VFOSSIL is a 80 by 24 monochrome text screen,  and any
program using VFOSSIL calls should be capable of operating within this level of
support.  By querying the VFOSSIL,  the full capabilities of a specific
implementation may be determined and used,  but all programs using VFOSSIL
should be capable of operating with the 80 by 24 monochrome text environment.


The organization of the video screen:

The virtual screen is organized in rows of columns of character/attribute
pairs,  hereafter referred to as cells.  The characters actually displayed
are located on the even addresses,  the attribute for each character is
located at character+1.

Regardless of the manner in which the video screen is actually organized,  the
programmer will view it as a a contiguous area of memory,  referred to as the
"logical video buffer" (LVB).  The LVB is (NumRow * NumCol) cells in length.


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
                                                                         Page  3

VFOSSIL installation:

The VFOSSIL appendage is installed via the standard FOSSIL external
application function.  The FOSSIL interrupt (14h) is issued with the
following parameters:

		AH = 7Eh	Install appendage
		AL = 81h	VFOSSIL application code
		DX = offset of VFOSSIL entry point
		ES = segment of VFOSSIL entry point

Upon return from the FOSSIL interrupt,  the following registers are
modified:

		AX = 1954h	FOSSIL signature
		BL = 81h	VFOSSIL application code
		BH = 01h - Installation was successful
		     00h - Installation  was unsuccessful

VFOSSIL removal:

The VFOSSIL appendage is removed via the standard FOSSIL external
application function.  The FOSSIL interrupt (14h) is issued with the
following parameters:

		AH = 7Fh	Remove appendage
		AL = 81h	VFOSSIL application code
		DX = offset of VFOSSIL entry point
		ES = segment of VFOSSIL entry point

Upon return from the FOSSIL interrupt,  the following registers are
modified:

		AX = 1954h	FOSSIL signature
		BL = 81h	VFOSSIL identification code
		BH = 01h - Removal was successful
		     00h - Removal was unsuccessful


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
                                                                         Page  4


VFOSSIL functions called via the standard FOSSIL interrupt (14h):

The following three functions are called via the standard FOSSIL interrupt,
int 14h.  All other VFOSSIL functions are called via the OS/2 compatible
direct call interface.

Subfunction 00h - Return VFOSSIL information

	Entry:	AH = 81h	VFOSSIL application code
		AL = 00h	VFOSSIL subfunction
		ES:DI = Far pointer to VFOSSIL information structure

	Exit:	AX = 1954h 	FOSSIL signature

    This function is used before calling the open function (sub-function 01h)
    to determine the characteristics of the VFOSSIL. Such things returned in
    the structure are current version level and number of functions supported.
    
    The format of the information structure filled in by this call is as
    follows:

	DW	Size of this structure,  in bytes,  including this field
	DW	VFOSSIL major version
	DW	VFOSSIL revision level
	DW	Highest VFOSSIL application function supported

Subfunction 01h - Open VFOSSIL

	Entry:	AH = 81h	VFOSSIL application code
		AL = 01h	VFOSSIL subfunction
		CX = Length of application function table (in bytes)
		ES:DI = Far pointer to application function table

	Exit:	BH = Highest VFOSSIL application function supported
		AX = 1954h	FOSSIL signature

	This VFOSSIL subfunction will initialize the table pointed to by
	ES:DI with far pointers to the VFOSSIL application services.  The
	number of far pointers initialized is equal to the value returned
	in register BH + 1.  Under no circumstances will the number of
	far pointers initialized exceed the value passed in register CX / 4.
	All other processing necessary to ready the VFOSSIL for use by the
	application program should be performed at this time.

Subfunction 02h - Close VFOSSIL

	Entry:	AH = 81h	VFOSSIL application code
		AL = 02h	VFOSSIL subfunction

	Exit:	AX = 1954h	FOSSIL signature

	This VFOSSIL function terminates all VFOSSIL operations,  and leaves
	the VFOSSIL in a state that allows for it to be removed from memory,
	or to be reinitialized via VFOSSIL function 01h.


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page  5


VFOSSIL application services:

All calls to VFOSSIL services are made in a manner identical to the OS/2 API
protocol.  All services are entered via a far call,  with parameters passed
via the stack.  All services return an error code in register AX.  The
parameters are pushed onto the stack Pascal-style,  from left to right.  The
parameters are passed on the stack in one of the three following ways:

    WORD   A one-word value pushed directly onto the stack

    DWRD   A double-word value pushed directly onto the stack
           (low word first,  followed by the high word)

    PTR    A far pointer to a memory area.  Far pointers are passed
           as double-word values,  segment followed by offset.

Single-word and double-word input parameters are always passed as WORD and
DWRD.  If the service returns information in the parameter field itself,
then it is pushed as a PTR,  even if the object is a WORD or a DWRD.  Variable
length parameters,  such as data structures or ASCIIZ strings, are always
passed as PTR objects.

All cursor coordinates are expressed as zero (0) based numbers.

Each VFOSSIL service requires a "handle" parameter as the last parameter
passed to the service.  At this time,  zero (0) is the only valid handle.

The actual addresses used to call the application services are contained in
the address table filled in by the VFOSSIL initialization call described
above.  All addresses are in far (segment/offset) format.  Here is the format
of the application service address table:

Table	+00h	VioGetMode		Query current video mode
	+04h	VioSetMode		Set video mode
	+08h	VioGetConfig		Query video hardware configuration
	+0Ch	VioWrtTTY		Write data in TTY mode
	+10h	VioGetANSI		Query current ANSI state
	+14h	VioSetANSI		Set ANSI state
	+18h	VioGetCurPos		Query current cursor position
	+1Ch	VioSetCurPos		Set cursor position
	+20h	VioGetCurType		Query current cursor parameters
	+24h	VioSetCurType		Set cursor parameters
	+28h	VioScrollUp		Scroll screen up
	+2Ch	VioScrollDn		Scroll screen down
	+30h	VioReadCellStr		Read cell string from display
	+34h	VioReadCharStr		Read char string from display
	+38h	VioWrtCellStr		Write cell string
	+3Ch	VioWrtCharStr		Write char string (existing attributes)
	+40h	VioWrtCharStrAtt	Write char string (constant attributes)
	+44h	VioWrtNAttr		Replicate attribute
	+48h	VioWrtNCell		Replicate cell
	+4Ch	VioWrtNChar		Replicate char


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page  6


VioGetMode - Query current video mode


Parameters:

	PTR	Pointer to a video mode data structure
	WORD	VIO handle (must be 0)


Video mode data structure:

	DW	Structure length (including this field)
	DB	Mode characteristics
		-------0	Monochrome/printer adapter
		-------1	Other adapter
		------0-	Text mode
		------1-	Graphics mode
		-----0--	Enable color
		-----1--	Disable color (black and white)
	DB	Number of colors supported by the display
		1 =  2 colors
		2 =  4 colors
		4 = 16 colors
	DW	Number of text columns
	DW	Number of text rows
	DW	Reserved
	DW	Reserved
	DD	Reserved


A partial video mode buffer may be specified.  VFOSSIL returns only the data
that will fit into the buffer.  The minimum buffer length is 3,  and the
maximum buffer length is 12.  Partial fields are not returned.


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	382 - Buffer too small
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page  7


VioSetMode - Set video mode


Parameters:

	PTR	Pointer to a video mode data structure (see VioGetMode)
	WORD	VIO handle (must be 0)


A partial video mode buffer may be specified.  The minimum buffer length is 3,
and the maximum buffer length is 12.  Partial fields are not supported.  The
remaining fields are set to default values.


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	355 - Unsupported mode
	382 - Buffer too small
	421 - Invalid VIO parameter
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page  8


VioGetConfig - Query video hardware configuration


Parameters:

	PTR	Pointer to a video configuration data area
	WORD	VIO handle (must be 0)


Video configuration data area:

	DW	Structure length (includes this field)
	DW	Adapter type
		0 = Monochrome/printer
		1 = CGA
		2 = EGA
		3 = VGA
		7 = 8514A
	DW	Display type
		0 = Monochrome
		1 = Color
		2 = Enhanced color
		9 = 8514
	DD	Adapter memory size


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	382 - Buffer too small
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page  9


VioWriteTTY - Write data in TTY mode


Parameters:

	WORD	Pointer to a character string that VFOSSIL will write
		to the screen
	WORD	String length
	WORD	VIO handle (must be 0)


This service writes a string to the video screen in TTY mode.  The characters
CR,  LF,  BS,  TAB,  and BELL are interpreted as control values rather than
being display as values.  If ANSI mode has been enabled (see VioGetANSI,  
VioSetANSI),  then ANSI control sequences are also interpreted as control 
strings.  In ANSI mode,  this service is not required to be reentrant,  and
should not be called when a MS/DOS function is in progress.  When in non-ANSI
mode,  this service is required to be reentrant,  and may be called from 
within a MS/DOS function.  If the write goes beyond the end of a line,  it
continues at the start of the next line.  The write terminates at the end of
the screen.  The cursor is left positioned at the next character position to
be written.


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page 10


VioGetANSI - Query current ANSI state


Parameters:

	PTR	Pointer to a one-word field in which VFOSSIL will return the
		current ANSI state:
			0 = Off
			1 = On 
	WORD	VIO handle (must be 0)


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page 11


VioSetANSI - Set ANSI state


Parameters:

	PTR	Pointer to a one-word field indicating how ANSI processing
		is to be set:
			0 = Off
			1 = On 
	WORD	VIO handle (must be 0)


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	421 - Invalid VIO parameter
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page 12


VioGetCurPos - Query current cursor position


Parameters:

	PTR	Pointer to a one word field in which VFOSSIL will return
		the current cursor row
	PTR	Pointer to a one word field in which VFOSSIL will return
		the current cursor column
	WORD	VIO handle (must be 0)


This service returns the current cursor position.  Cursor coordinates are
zero based.


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page 13


VioSetCurPos - Set cursor position


Parameters:

	WORD	Desired cursor row
	WORD	Desired cursor column
	WORD	VIO handle (must be 0)


This service sets the cursor position to the zero based coordinates specified
by the parameters.  If either of the parameters is invalid,  the cursor
position is left unchanged.


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	358 - Invalid row value
	359 - Invalid column value
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page 14


VioGetCurType - Query current cursor parameters


Parameters:

	PTR	Pointer to a cursor type data area
	WORD	VIO handle (must be 0)


Cursor type data area:

	DW	Cursor start line
	DW	Cursor end line
	DW	Cursor width (always 1)
	DW	Cursor attribute (-1 = hidden)


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page 15


VioSetCurType - Set cursor parameters


Parameters:

	PTR	Pointer to a cursor type data area (see VioGetCurType)
	WORD	VIO handle (must be 0)


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	421 - Invalid VIO parameter
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page 16


VioScrollUp - Scroll screen up


Parameters:

	WORD	Top row of the scroll area
	WORD	Left column of the scroll area
	WORD	Bottom row of the scroll area
	WORD	Right column of the scroll area
	WORD	Number of rows to scroll.  A value of -1 causes the scroll
		area to be cleared.
	PTR	Pointer to a char/attr cell that is used to fill the scroll
		area.
	WORD	VIO handle (always 0)


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	358 - Invalid row value
	359 - Invalid column value
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page 17


VioScrollDn - Scroll screen down


Parameters:

	WORD	Top row of the scroll area
	WORD	Left column of the scroll area
	WORD	Bottom row of the scroll area
	WORD	Right column of the scroll area
	WORD	Number of rows to scroll.  A value of -1 causes the scroll
		area to be cleared.
	PTR	A pointer to a char/attr cell that is used to fill the scroll
		area.
	WORD	VIO handle (always 0)


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	358 - Invalid row value
	359 - Invalid column value
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page 18


VioReadCellStr - Read cell string from display


Parameters:

	PTR	Pointer to a buffer into which the cell string is to be
		placed
	PTR	Pointer to a one-word field which,  upon entry,  specifies
		the length of the cell buffer (in bytes),  and,  on return,
		contains the number of bytes actually read.  Each cell
		occupies two bytes,  so the number of cells read is equal to
		half of the buffer length specified.
	WORD	Row where the read is to start
	WORD	Column where the read is to start
	WORD	VIO handle (always 0)


If the read request extends beyond the end of the line,  it continues at the
first column of the next line.  If an attempt is made to read past the end of
the screen,  the read operation terminates and the length field is set to the
actual number of bytes read.


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	358 - Invalid row value
	359 - Invalid column value
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page 19


VioReadCharStr - Read character string from display


Parameters:

	PTR	Pointer to a buffer into which the character string is to be
		placed
	PTR	Pointer to a one-word field which,  upon entry,  specifies
		how many characters are to be read,  and,  on return,
		contains the number of characters actually read.
	WORD	Row where the read is to start
	WORD	Column where the read is to start
	WORD	VIO handle (always 0)


If the read request extends beyond the end of the line,  it continues at the
first column of the next line.  If an attempt is made to read past the end of
the screen,  the read operation terminates and the length field is set to the
actual number of characters read.


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	358 - Invalid row value
	359 - Invalid column value
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page 20


VioWrtCellStr - Write a cell string


Parameters:

	PTR	Pointer to the cell string to be written
	WORD	Cell string length.  Since each cell occupies two bytes,
		this number is twice the number of cells to be written.
	WORD	Row at which write is to begin
	WORD	Column at which write is to begin
	WORD	Vio handle (must be 0)


If the write request extends beyond the end of the line,  it continues at the
first column of the next line.  If an attempt is made to write past the end of
the screen,  the write operation terminates.


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	358 - Invalid row value
	359 - Invalid column value
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page 21


VioWrtCharStr - Write a character string,  using existing attributes


Parameters:

	PTR	Pointer to the character string to be written
	WORD	Character string length
	WORD	Row at which write is to begin
	WORD	Column at which write is to begin
	WORD	Vio handle (must be 0)


The attributes of the display cells whose characters are replaced are not
modified.  If the write request extends beyond the end of the line,  it
continues at the first column of the next line.  If an attempt is made to
write past the end of the screen,  the write operation terminates.


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	358 - Invalid row value
	359 - Invalid column value
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page 22


VioWrtCharStrAtt - Write a character string,  using constant attribute


Parameters:

	PTR	Pointer to the character string to be written
	WORD	Character string length
	WORD	Row at which write is to begin
	WORD	Column at which write is to begin
	PTR	Pointer to the display attribute to be used with each
		character written
	WORD	Vio handle (must be 0)


If the write request extends beyond the end of the line,  it continues at the
first column of the next line.  If an attempt is made to write past the end of
the screen,  the write operation terminates.


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	358 - Invalid row value
	359 - Invalid column value
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page 23


VioWrtNAttr - Replicate an attribute byte,  leaving characters unchanged


Parameters:

	PTR	Pointer to the display attribute to be replicated
	WORD	Replication count
	WORD	Row at which write is to begin
	WORD	Column at which write is to begin
	WORD	Vio handle (must be 0)


The characters contained in the display cells whose attributes are replaced
are not modified.  If the write request extends beyond the end of the line,
it continues at the first column of the next line.  If an attempt is made to
write past the end of the screen,  the write operation terminates.


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	358 - Invalid row value
	359 - Invalid column value
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page 24


VioWrtNCell - Replicate a cell


Parameters:

	PTR	Pointer to the cell to be replicated
	WORD	Replication count
	WORD	Row at which write is to begin
	WORD	Column at which write is to begin
	WORD	Vio handle (must be 0)


If the write request extends beyond the end of the line,  it continues at the
first column of the next line.  If an attempt is made to write past the end of
the screen,  the write operation terminates.


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	358 - Invalid row value
	359 - Invalid column value
	436 - Invalid VIO handle


VFOSSIL - An OS/2 Subset Video FOSSIL Appendage                         FSC-0021
Application Services                                                     Page 25


VioWrtNChar - Replicate an character,  leaving attributes unchanged


Parameters:

	PTR	Pointer to the character to be replicated
	WORD	Replication count
	WORD	Row at which write is to begin
	WORD	Column at which write is to begin
	WORD	Vio handle (must be 0)


The attributes contained in the display cells whose characters are replaced
are not modified.  If the write request extends beyond the end of the line,
it continues at the first column of the next line.  If an attempt is made to
write past the end of the screen,  the write operation terminates.


Error codes returned:

	  0 - Successful completion
	116 - Internal VIO failure
	358 - Invalid row value
	359 - Invalid column value
	436 - Invalid VIO handle