1. INTRODUCTION

  Desktop PC user are generally aware of the disadvantages about Desktop PC's
  Monitor display - small screen size and high price.  For better effect, you
  would have to pay more for a larger VGA or multiscan monitor (generally VGA
  monitor is 14 inches).

  Now, the TV_Adaptor provides an excellent solution to all these problems by
  converting Desktop PC's display signal to NTSC(or PAL) standard video sig
  -nal.  Enable you to watch your Desktop PC's monitor display in TV monitor,
  TV projector or recorded it in VCR for future viewing.

  (1) Basic concepts

     Video source

     More video systems use AV composite signal to carry image data.  Several
     popular standards, for example, NTSC, PAL, and SECAM are widely used over
     the world. NTSC, with 525 scan lines definition, is used in North America
     and in most areas of the world;  PAL, with 625 scan lines definition, is
     used in European countries.   The TV_Adaptor has two versions supporting
     either NTSC or PAL systems.

     The difference between VGA and TV signals

     VGA, the primary display device supported by Desktop PC, is by far the be
     -tter display card on the low-end PC graphics market.   It possesses gray
     level capability and circuits for displaying real-world images instead of
     artificial computer graphics.   The standard VGA is compatible with CGA,
     EGA, and can be operated in 320*200 resolution 256 colors / 64 gray, 640*
     480 resolution 256 colors. The differences between VGA and TV signals are
     (1) Horizontal frequency (VGA is 31.5KHZ, TV is 15KHZ).  (2) Vertical fre
     -quency (70HZ and 60HZ). (3) Interlace (TV) and Noninterlace (VGA) scan.

     Hotkey and TSR program

     Programs such as SIDEKICK or DOS graphic execution files are executed and
     kept in PC's RAM; and can be reactive later when needed.   Those programs
     are called TSR (Terminated,Stay and Resident) program.  TSR allows you to
     activate it along with hotkey.  TV_Adaptor provides TSR program, Once the
     program is installed, you may bring up the display switch function by pre
     -ssing the predefined hotkey (described in the next section).

#

  (2) Introduction to TV_Adaptor

     TV_Adaptor works as an interface between VGA and TV signals,  converting
     VGA signal to TV standard (NTSC or PAL) signal.  The TV_Adaptor consists
     of two parts  :  TV_Adaptor controller (hardware part) and the TV_Adaptor
     driver (software part).

     TV_Adaptor controller:

     It has been our design goal, not just smaller in electric circuit and
     layout, but in the appearance itself (shown as Fig.1). It's smaller than
     a man's hand, light, short, and easy to use.  It is perfectly fit to use
     together with Desktop PC.  The TV_Adaptor controller receives the signal
     from VGA card external connector with the format of RGB signals, and then
     converts it becomes composite NTSC (or PAL) signal to Video output port.


     Fig. 1








     TV_Adaptor driver:

     Once TSR (terminated, Stay and Resident) program is installed.  it stays
     in system's memory. Just like you - use the Hotkey to toggle the Desktop
     PC's display between Mono mode and VGA mode, you may use the hotkey to
     activate the driver and toggle the Desktop PC's display between VGA fre-
     quency and NTSC (PAL) frequency. It takes 6300 bytes - of the systems's
     memory.


    NOTE : 1) VGA (Video Graphics Array) : A computer monitor display standard
              which provides for resolution as high as 640*480 pixels and 256
              color out of a pallette of 262,144 colors.

           2) NTSC (National Television standard Committe) : The organization
              that specified the television standard used in North America and
              several other countries.
              ; 525 lines, 60 frames per Second, 2 frames per field.

           3) PAL (Phase Alternating Lines) : The television standard used in
              most of Europe (with the exception of France and Russia, which
              use SECAM).  The PAL standard is 50 frames per second, with 625
              lines.
     #


 (3) How TV_Adaptor driver perform its role with Desktop PC

  Before activating the TV_Adaptor driver with a hotkey, it is important to
  learn how the TV_Adaptor driver works. Fig.2 illustrates how you choose your
  display in Desktop PC. You can use the driver, supplied by VGA BIOS manufac
  -turer, or the hotkey (defined by manufacturer) toggling display between VGA
  monitor and TV While using TV_Adaptor.  TV set takes the place of VGA. Fig.3
  illustrates the situation.

  Fig. 2



  Fig. 3




2. SYSTEM PREPARATION

  (1) Check out what you get in your hand

   You should receive the following items in your shipping package :

   * TV_Adaptor controller
   * Power adaptor
   * AV shielded cable (4.5m)
   * TV_Adaptor driver in 2DD 720K floppy disk : (including)
     # Setpath.exe  : Set AutoSave Path
     # AutoSave.exe : Enable AutoSave CRTC Parameter Function
     # Disable.exe  : Disable Autosave CRTC Parameter Function
     # PCV.com      : TSR driver (converter VGA signal to TV signal)
     # Readme.doc   : A short introduction to TV_Adaptor
     # Install.exe  : Auto install TV_Adaptor driver to your computer
                      local hard disk
     # TV.bat       : Startup TSR driver for using TV display while hard
                      disk noninstalled
     # Vga.bat      : Startup TSR driver for using VGA display while hard
                      disk noninstalled

#

3. INSTALLATION

  (1) Hardware installation

    There are five steps for you to install TV_Adaptor controller.

  STEP1:
    Plug TV_Adaptor controler in  PC's external DB15 VGA output connector.

  STEP2:
    Tighten the rotating screwer of TV_Adaptor connector.

  STEP3:
    Connect power adaptor to TV_Adaptor and make sure the power supplier is
    connected.

  STEP4:
    Connect AV cable from your TV video input port to TV_Adaptor output port.
    Check out what is the channel you have connected.

    NOTE: AV cable (composite Video Signal) contains the intensity, color
           and timing informations necessary for video.

  STEP5:
    Power on your PC, wait until DOS prompt is shown on the screen.

  STEP6:
    Power in your TV set, Select the AV channel to match with STEP5.

    NOTE: To match with NTSC version TV_Adaptor controller, you should use the
          TV with NTSC system (or Multisystem) same as PAL version.


  (2) Software installation

    Before continue software installation below, please check whether if there
    is any message showing on display. We call the PC which with message on
    display as A type PC, and the others which without any message as B type
    PC.  This is the result of different display method that produced by
    different manufacturer. If you power on, When VGA external connector of
    Desktop PC is connected to VGA monitor, you will find:

    Type Install TV  (if have hard disk)
         Install VGA
#






5. TROUBLE SHOOTING

   (1) Trouble: Nothing displayed in TV

    Solution:

     1. Make sure the DC power adaptor was added into TV_Adaptor controller.

     2. Make sure you choose the AV channel in TV which is the same as the
        video cable you plugged in.

     3. Make sure the TV_Adaptor controller is plugged firmly in your Desktop
        PC's external VGA connector.

     4. Make sure the video cable connects between TV_Adaptor controller and
        TV set.

     5. Make sure which kind of display mode you are in.  There are two kinds
        of display --- VGA and TV.   Please review the section of software
        installation.

     6. The reason may be that you release the TV_Adaptor driver without chang
        -ing back to VGA. Use the HOTKEY supplied by VGA BIOS manufactures and
        switch to VGA.

   (2) Trouble: System shuts down while using HOTKEY

    Solution:

     1. Avoid using HOTKEY to toggle mode (change display from VGA to TV or TV
        to VGA) while DOS system is loading the application software.  Do not
         use HOTKEY until loading is finished.

     2. Conflict with mouse driver . Please install the mouse driver before
        installing the TV_Adaptor driver.

     3. Conflict with other TSR program.  Please release them while using TV_
        Adaptor driver.

     4. Caused by your application softwares.  Check and see what happens with
        -out the TV_Adaptor driver installed.

   (3) Trouble: Cursor disappears

    Solution:

     1. While switching to TV mode, the cursor will disappear in some applicat
        -tion software such as PE2.  We are trying to resolve it and shall have
        a good solution.

   (4) Trouble: Some character's attribute (color) will change while switching
                to TV MODE

    Solution:

     1. Switch to TV mode before activating application software.

   (5) Trouble: Vertical out of lock (TV screen jumping up and down) or TV
                become monochrome

    Solution:

     1. Check and make sure you choose the same video system (either NTSC or
        PAL) in the TV_Adaptor driver.

     2. TV_Adaptor out of lock with TV SUBCARRIER 3.58Mhz signal, adjust TV_
        Adaptor's internal variable capacitor to match TV signal.  (Having no
        experience, don't do it yourself).

   (6) Trouble: Malfunction of HOTKEY

    Solution:

     1. Check if the TV_Adaptor driver is installed or not (use the helping
        function described in the section "TV_Adaptor driver function").

     2. HOTKEY entry is kept away by other application software (such as
        windows) Switch to TV mode first. then enter the application software.

     3. Make sure your display is in VGA mode or TV mode. In case it is in VGA
        mode, the HOTKEY will be seen in malfunction.

     4. Reactivate TV_Adaptor driver with HOTKEY, then you will know what the
        trouble is.

   (7) Trouble: odd line is lost

    Solution:

     1. When the TV_Adaptor works in a non-interlace mode, the odd line will
     get lost.  TV_Adaptor can support in an interlace mode only when your PC's
     VGA chip has IRQ2 (interrupt 0Ah).  Usually the TV_Adaptor can support an
     interlace mode for most PC and VGA chip.

   (8) Trouble: The toppest and lowest part of display is clipped for 640*480
       NTSC mode

    Solution:

     1. This phenomenon exists due to the fact that the NTSC mode can not dis
        -play widely enough for the VGA mode with 480 horizontal lines. It can
        just display 470 lines (different from the TV).   Now you can see the
        whole 480 lines with the adjustment of HOTKEY with the best view.  In
        PAL mode, this trouble does not happen at all.

   (9) Trouble: Flicks of blinking in TV

    Solution:

     1. TV_Adaptor driver may conflict with other TSR program such as HIMEM.
        -sys installed with DOS CONFIG.SYS.  Remove other TSR program. If the
        application do not need the extended memory.

     2. Caused by different interlaced fields.  VGA mode is a noninterlaced
        type with refresh rate 60 HZ to 70 HZ per second.  While NTSC is an
        interlaced field, one field, its refresh rate 60 HZ (60 fields) per
        second, or 30 HZ (30 frame) per second.  So everything in VGA monitor
        will be solved down while transferred to TV.  (check our Appendix B to
        be detailed)  This is the reason why a contrasting horizontal color
        line flick more intensely than a dot or a table of changing color.

   (10) Trouble: Ghost or crosstalk esp. in text and color border.

    Solution:

     1. Because the speed of computer display faster than TV does, the trouble
        happens while TV_Adaptor transfers the faster signal to higher speed
        VGA signal.

#

   Appendix A: SPECIFICATION

     Dimensions
     * xxx mm(L) * xxx mm (V)

     Power consumption
     * 5 to 8 Volt DCV 120 ma

     Input signal
     * Analog R G B signal from VGA DB15 pin connector, 0.7 Volt peak to peak.

     Output signal
     * U.S. standard (NTSC)
       - Composite color NTSC : 1 Volt peak to peak (AV connector)

     * European standard (PAL)
       - Composite color PAL  : 1 Volt peak to peak (AV connector)

     Software
     * TV_Adaptor driver

     System requirements
     * PC with external 15 pin VGA connector
     * IBM PC/XT, AT or compatible with VGA card.
     * VGA support Tseng ET-3000,ET-4000, Trident 8800,8900,9000, Paradise VGA
       serial, OAK 037,067,077, Tamarack TD3588,TD3688, Acumos AVGA1,2,ATI,V7
       Cirrus
     * MS-DOS 3.0 or higher
     * 640k byte memory or larger

#

   Appendix B: How to make the most of TV_Adaptor

?    1. When switching between LCD panel and TV, do always use the HOTKEY as
?      follow:
?
?              LCD panel -----> VGA -----> TV
?                          or
?
?              TV ------------> VGA -----> LCD panel

    2. While presenting your demonstration with TV_Adaptor, you'd better not
       have a picture with a single horizontal light line, Let it be double,
       or even triple.  Because TV's scans allways interlaced, so the demo
       program must be designed with many different colors, instead of just
       a white line.

    3. Adjust the TV color as dark as possible, because a paler color may let
       your eyes feel the blinking of the color when the picture is scan int-
       erlaced.

    Above are three recommendations to make the best of TV_Adaptor so as to
    help you present your demonstration as good as possible.