TABLE D-1/Q.767 (sheet 1 of 6)

Timers used in ISUP-R

| Symbol | Time-out value | Significance | Cause for initiation | Normal termination | At expiry | Section |
| --- | --- | --- | --- | --- | --- | --- |
| T1 | 15-60 seconds | Local | When release message is sent | At the receipt of release complete message | Re-transmit release message and start timer T1 | 2.2 — 2.3.1 2.10.6 |
| T2 | 3 min | Dual | When suspend request controlling exchange receives suspend (user) message | At the receipt of resume (user) message at controlling exchange | Initiate release procedure | 2.5.1.1 2.5.2.1 2.5.3 |
| T3 | 2 min |
| Not used on the international interface |
|  | 2.6 |
| T4 |
|  | Not used on the international interface |
|  | 2.7.1 2.7.2 |
| T5 | 5-15 min | Local | When initial release message is sent | At receipt of release complete message | Send reset circuit message, alert maintenance personnel and remove the circuit from service, stop T1 start T17. Procedure continues until maintenance intervention occurs | 2.2 2.3.1 2.10.6 |
| T6 | Covered in Rec. Q.118 | Dual | When controlling exchange receives suspend (network) | At the receipt of resume (network) message | Initiate release procedure | 2.5.1.3 2.5.2.3 — 2.5.3 |

TABLE D-1/Q.767 (sheet 2 of 6)

Timers used in ISUP-R

| Symbol | Time-out value | Significance | Cause for initiation | Normal termination | At expiry | Section |
| --- | --- | --- | --- | --- | --- | --- |
| T7 | 20-30 s | Dual | When the latest address message is sent | When the condition for normal release of address and routing information is met (receipt of ACM, CON messages) | Release all equipment and connection (send release message with cause 31) | 2.1.1.1 2.1.4.4 2.1.4.8 2.1.2.1 f) 2.10.8.3 |
| T8 | 10-15 s | Local | When transit or incoming international exchange receives initial address message requiring continuity check on this circuit, or indicates that continuity check has been performed on a previous circuit | At receipt of continuity message | Release all equipment and connection into national network (send release message with cause 31) | 2.1.8 2.10.8.3 |
| T9 | Interval specified in Rec. Q.118 | Dual | When national controlling or outgoing international exchange receives ACM | At the receipt of answer | Release connection and send back release message with cause 19 | 2.1.4.4 2.1.7.2 2.1.7.3 2.10.8.3 |
| T10 | 4-6 s | Dual | When last digit is received in interworking situations | At the receipt of fresh information | Send address complete message | 2.1.2.1 e) 2.1.4.8 |
| T11 | 15-20 s | Dual | When latest address message is received in interworking situations | When ACM is sent | Send address complete message | 2.1.4.8 |

TABLE D-1/Q.767 (sheet 3 of 6)

Timers used in ISUP-R

| Symbol | Time-out value | Significance | Cause for initiation | Normal termination | At expiry | Section |
| --- | --- | --- | --- | --- | --- | --- |
| T12 | 15-60 s | Local | When blocking message in sent | At receipt of blocking acknowledgement | Re-transmit blocking message and start T12 | 2.10.4 |
| T13 | 5-15 min | Local | When initial blocking message is sent | At receipt of blocking acknowledgement | Transmit blocking message, alert maintenance personnel and start T13; stop T12. Procedure continues until maintenance intervention occurs | 2.10.4 |
| T14 | 15-60 s | Local | When unblocking message is sent | At receipt of unblocking acknowledgement | Re-transmit unblocking message and start T14 | 2.10.4 |
| T15 | 5-15 min | Local | When initial unblocking message is sent | At receipt of unblocking acknowledgement | Re-transmit unblocking message and alert maintenance personnel, start T15, and stop T14. Procedure continues until maintenance intervention occurs | 2.10.4 |
| T16 | 15-60 s | Local | When reset circuit message is sent not due to the expiry of Timer T5 | At the receipt of the acknowledgement (RLC message) | Re-transmit reset circuit message start T16 | 2.10.3.1 |
| T17 | 5-15 min | Local | When initial reset circuit message is sent | At the receipt of the acknowledgement | Alert maintenance personnel, retransmit reset circuit message, start T17 and stop T16. Procedure continues until maintenance intervention occurs | 2.10.3.1 |

TABLE D-1/Q.767 (sheet 4 of 6)

Timers used in ISUP-R

| Symbol | Time-out value | Significance | Cause for initiation | Normal termination | At expiry | Section |
| --- | --- | --- | --- | --- | --- | --- |
| T18 | 15-60 s | Local | When group blocking message is sent | At receipt of group blocking acknowledgement | Re-transmit group blocking message and start T18 | 2.10.4 |
| T19 | 5-15 min | Local | When initial group blocking message is sent | At receipt of group blocking acknowledgement | Re-transmit group blocking message, alert maintenance personnel, start T19 and stop T18. Procedure continues until maintenance intervention occurs | 2.10.4 |
| T20 | 15-60 s | Local | When group unblocking message is sent | At receipt of group unblocking acknowledgement | Re-transmit group unblocking message and start T20 | 2.10.4 |
| T21 | 5-15 min | Local | When initial group unblocking message is sent | At the receipt of group unblocking acknowledgement | Re-transmit group unblocking message, alert maintenance personnel, start T21 and stop T20. Procedure continues until maintenance intervention occurs | 2.10.4 |
| T22 | 15-60 s | Local | When circuit group reset message is sent | At the receipt of the acknowledgement | Re-transmit circuit group reset message, start T22 | 2.10.3.2 |

TABLE D-1/Q.767 (sheet 5 of 6)

Timers used in ISUP-R

| Symbol | Time-out value | Significance | Cause for initiation | Normal termination | At expiry | Section |
| --- | --- | --- | --- | --- | --- | --- |
| T23 | 5-15 min | Local | When initial circuit group reset message is sent | At receipt of the acknowledgement | Alert maintenance personnel and start T23, re-transmit circuit group reset message, stop T22. Procedure continues until maintenance intervention occurs | 2.10.3.2 |
| T24 | < 2 s | Local | When check tone is sent | At the receipt of backward check tone | Send continuity message with failure indication and: a) start T25 if continuity check was asked in an IAM and make automatic repeat attempt, or b) start T26 if continuity check was asked in a CCR | Rec. Q.724, § 7.4.1 |
| T25 | 1-10 s | Local | When initial continuity check failure is detected |
| Send CCR message and repeat continuity check | Rec. Q.724, § 7.3 |
| T26 | 1-3 min | Local | When second or subsequent continuity check failure is detected |
| Send CCR message and repeat continuity check | Rec. Q.724, § 7.3 |
| T27 | 4 min | Local | When continuity check failure indication is received | At receipt of continuity check request message | Send reset circuit message; start T16 and T17 | 2.1.8 |
| T28 |
|  | Not used ont the international interface |
|  | 2.9.3.2 |

TABLE D-1/Q.767 (sheet 6 of 6)

Timers used in ISUP-R

| Symbol | Time-out value | Significance | Cause for initiation | Normal termination | At expiry | Section |
| --- | --- | --- | --- | --- | --- | --- |
| T29 | 300-600 ms | Local | Congestion indication received when T29 not running |
| New congestion indication will be taken into account | 2.11.2 |
| T30 | 5-10 s | Local | Congestion indication received when T29 not running |
| Restore traffic by one step if not yet at full load and start T30 | 2.11.2 |
| T31 |
|  | Not used on the international interface |
|  | 3.7.2 3.7.3 3.7.4 |
| T32 |
|  | Not used on the international interface |
|  | 3.7.5 |
| T33 | 12-15 s |
| When send INR | On receipt of INF | Release call, alert maintenance personnel (cause 31) | 2.1.6.2 2.9.7 Q.730 |
| T34 |
|  | Not used on the international interface |
|  | 2.9.3.2 |
| T35 | 15-20 s | Dual | At receipt of the latest digit (< > ST) and before the minimum or fixed number of digits have been received | At receipt of ST or when the minimum or fixed number of digits have been received | Send release message (cause 28) | 2.2.5 2.10.8.3 |
| T36 | 10-15 s | Local | When transit or incoming international exchange receives continuity check request message | At receipt of continuity or release message | Release all equipment, sent reset circuit message, start T16 and T17 | 2.1.8 |
| T37 |
|  | Not used on the international interface |
|  | T38 (only for White book) | Interval specified in Q.118 |
| When the incoming international exchange sends to the preceding exchange a suspend (network) message | At receipt of resume (network) or release message | Send release message (cause 102) | 2.4.1 2.4.2 2.4.3 |